## Slide 1
芯片设计流程
iEDA课题组

## Slide 2
芯片设计流程
设计思路
设计内容
设计方式
01
02
03
04

## Slide 3: 手机芯片模块
https://zhidao.baidu.com/question/122566460.html

## Slide 4: 芯片设计目标
https://semiwiki.com/eda/6349-how-to-nail-your-ppa-tradeoffs/
CPU系列 | 酷睿i9 11代系列
CPU主频 | 3.5GHz
最高睿频 | 5.3GHz
三级缓存 | 16MB
插槽类型 | LGA 1200
核心数量 | 八核心
线程数 | 十六线程
热设计功耗 | 125W
晶体管数量 | 70亿
设计目标（PPA）
  Performance 性能
  Power 功耗
  Area 面积

## Slide 5: 处理器芯片设计：从指令集到芯片
处理器架构设计：将指令集手册定义到功能实例化，形成设计文档；
功能开发：将设计文档开发成RTL级逻辑运算代码；
版图设计：用EDA工具将设计好功能等RTL代码物理化成GDS版图；
芯片制造：将设计好的版图通过光刻制造封装形成芯片；
工程开发
RTL代码
EDA工具
芯片版图
指令集手册
设计文档
微架构设计
制造封装
芯片产品

## Slide 6: 芯片设计层次
Chip Design Level
Gate Level
Transistor Level
Register Transfer Level
System Level
Layout Level
Mask Level
System Level
Register Transfer Level
Gate Level
Transistor Level
Layout Level
Mask Level
Chip Level
PCB Level

## Slide 7: EDA问题拆解——模块
逻辑综合 (Logic Synthesis)
物理设计 (Physical Design)
版图后处理 (Layout Post Processing)
单元库设计 (Standard Cell Library)
签核分析 (Signoff Analysis)
电路仿真 (Circuit Simulation)
物理验证 (Physical Verification)
封装测试 (Package and Test)
EDA数据库 (EDA Data Base)
芯片测试集 (Chip Benchmark)
GUI和智能流程 (GUI and Flow)
EDA Platform
EDA Modules
Logic Synthesis
Physical Design
Circuit Simulation
Signoff Analysis
Layout Processing
……
……
Standard Cell Library
Physical Verification
Test
Package
EDA Flow
Logic Synthesis
Layout Processing
Standard Cell Library
Physical Verification
Package
Design
Verification
EDA Platform
EDA Modules
Logic Synthesis
Physical Design
Circuit Simulation
Signoff Analysis
Layout Processing
……
……
Standard Cell Library
Physical Verification
Test
Package
EDA Flow
Logic Synthesis
Layout Processing
Standard Cell Library
Physical Verification
Manufacture Package
Design
Verification

## Slide 8: EDA问题拆解——模块
Physical Design
Circuit Simulation
Signoff Analysis
……
Test
Logic Synthesis
Layout Processing
Standard Cell Library
Physical Verification
Manufacture Package
Functional Design
System Architecture
Functional
Verification
Design
Verification

## Slide 9: 设计过程
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Layout Processing
Fabrication
Architectural Design
Package and Test
D
X
Y
module conv;
reg [31:0] m[0:8192];
reg [12:0] pc;
reg [31:0] acc;
reg[15:0] ir;
always
begin
ir = m[pc];
if(ir[15:13] == 3b’000)
pc = m[ir[12:0]];
else if (ir[15:13] == 3’b010)
acc = -m[ir[12:0]];
...
Timing DRC
DRC
ERC
LVS

## Slide 10: EDA工具链组成
Logic Synthesis
Logic Compiling
Logic Optimization
Tech Mapping
ATPG/BIST
Layout Processing
RET/OPC/ILT
Mask Generation
Physical Design
Floorplan
Placement
Clock Tree Synthesis
Routing
ECO
Physical Verification
ERC
DRC (MP)
LVS
Std Cell Lib
Device Modeling
Parasitic Extraction
DRC/LVS
Specifications
Architectural Design
Functional Design
Timing Optimization
ESD/CD
Analysis
Timing Analysis
RC Extraction
Power
Noise
IR Drop
Simulation
Simulation (Circuit)
Emulation (System)
Fabrication
Package and Test
Chip
module conv;
reg [31:0] m[0:8192];
reg [12:0] pc;
reg [31:0] acc;
reg[15:0] ir;
always
begin
ir = m[pc];
if(ir[15:13] == 3b’000)
pc = m[ir[12:0]];
else if (ir[15:13] == 3’b010)
Verification
Functional Verification
Formal Verification
PCB
Equivalence Check
Post Simulation

## Slide 11: 设计过程
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
需求要素
  Target market,
  Desired performance,
  Power targets,
  Interface IP requirements,
  Use cases
This input provides the foundation for a chip’s specification and architecture development.
Power requirements should be very detailed, identifying power domains; dynamic voltage and frequency scaling; adaptive voltage and frequency scaling; and power modes.
In addition, designers should specify die size, pin-count, IP configuration freeze and any custom IP requirements.
Requires computational power to run imaging algorithms to support virtual reality.
Requires two ARM A53 processors with coherent interconnect and should run at 600 MHz.
Requires USB 3.0, Bluetooth and PCIe 2nd gen interfaces.
Should support 1920x1080 pixel display with appropriate controller hen specifying a chip.

## Slide 12: 设计过程
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
https://www.chipverify.com/verilog/asic-soc-chip-design-flow

## Slide 13: 设计过程
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
IP Provision
3rd-party / In-house
Architecture Design Decision
System Specifications
Inputs:
Firmware, Application Code, RTL, Assertions, Design, Database, System C Models, High-Level Models, Test Benches
APIs
Structure
Behavioral H/W Descript
Instruction Set,
Simulator
High-Level Synthesis
Behavioral RTL
module conv;
reg [31:0] m[0:8192];
reg [12:0] pc;
reg [31:0] acc;
reg[15:0] ir;
always
begin
ir = m[pc];
if(ir[15:13] == 3b’000)
pc = m[ir[12:0]];
else if (ir[15:13] == 3’b010)
acc = -m[ir[12:0]];
...
Verification
Simulation

## Slide 14: 设计过程
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test

## Slide 15: 设计过程——逻辑综合
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
abcd f
0 0000 0
1 0001 1
2 0010 0
3 0011 1
4 0100 0
5 0101 1
6 0110 0
7 0111 0
Logic Representation
Logic Minimization
Factored Forms
Division
Don’t Cares
Set ports
Set regs
Read sdc
Create clock
Set area
…
Compilation
Library Definition
Elaboration
Binding
Logic Optimization
Constraint
module conv;
reg [31:0] m[0:8192];
reg [12:0] pc;
reg [31:0] acc;
reg[15:0] ir;
always
begin
ir = m[pc];
if(ir[15:13] == 3b’000)
pc = m[ir[12:0]];
else if (ir[15:13] == 3’b010)
acc = -m[ir[12:0]];
...
RTL
Library
z=0
z=1
00/0,01/0,11/0
00/1,01/1,10/1
11/0
10/1
FSM

## Slide 16: 设计过程——逻辑综合
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
Standard Cell Liberty
.svg, .cdl, .gds, .lib, .lef, .v
Symbol
(.svg)
Schematic
(.cdl)
Layout
(.gds)
Abstract
(.lef)
LVS
DRC
Netlist
(.v)
PEX
Extraction
GDS Extraction
Abstract
CDL Extraction
Draw
SPICE Model
Tech Device
Tech Design Rule
PEX Parameter
(.pex)
Liberate
Characterization
Liberty
(.lib)
Verification
Validation
Physical Design
Synthesis
Physical Design
Analysis
Standard Cell Library
  Symbol (.svg)
  Behavioral (.v)
  Physical
    Layout (.gds)
    Abstract (.lef)
  Transistor (.spi)
  Timing/Power (.lib)
  Functional
    Combinational
    Buffer
    Sequential
    Physical
  Type
    Voltage
    Drive Strength
    Size

## Slide 17: 设计过程——逻辑综合
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
Process Design Kit
  针对选择的每种类型门器件，对其进行Schematic设计，并进行电路仿真得到电学参数；
  选择工艺和器件模型，进行门器件Layout设计，获得GDS版图；
  对工艺提取技术约束TechFile，形成DRC/LVS和提取参数；
Process Design Kit
(Device, Schematic, Pcell, TechFile, DRC/LVS/RCX)
Device Primitives
(P/N Mos, BJTs, Diodes, Resistor, Capacitor)
Schematic Capture
Symbol & Schematic
Layout
Parameter Cell
Analog Simulation
SPICE Model
Tech File
(Layer Map, Layer Props, Symbolics, Connectivity)
Verification
(DRC, LVS, RCX)
Cell
Physical Design & Verification
Chip Assembly
Physical Verification
Standard Cell Liberty
.svg, .cdl, .gds, .lib, .lef, .v

## Slide 18: 设计过程——工艺映射
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
Logic
Re-Optimization
Tech Mapping
Equivalence Checking
Timing/Power Analysis
Test Logic Insertion
Physical Synthesis
Balance
Rewrite
Refactor
Resubsti-
tution
Desomposition
Partition
Simulation

## Slide 19: 设计过程——工艺映射
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test

## Slide 20: 设计过程——物理设计
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
Chart: 图表标题
Chart: 图表标题
Chart: 图表标题
Chart: 图表标题
Floorplan：确定Die和Core大小，确定IO位置，规划Macro的摆放，设计电源线，放置物理单元。
Placement：摆放标准单元至合法的位置，插入填充单元，进行时序优化，使得设计目标最优。
CTS：设计时钟网络，连接每个FF的时钟pin。实现时钟同步，功耗低等目标。
Routing：将连接单元pin的Net在规定的金属层的Track上实体化，使得线长短，时序功耗低，设计规则满足。

## Slide 21: 设计过程——物理设计
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
布图
布局
布线

## Slide 22: 设计过程——验证
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
Simulation Verification
Timing Verification
Geometric
(DRC, ERC)
Extraction
(LVS)
Formal Verification
Formal
Simulation
Timing
DRC/ERC
LVS

## Slide 23: 设计过程——验证
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
Timing
Noise
IR Drop
Power
RC Extraction
IN1
CLK1
IN2
CLK2
GATE
OUT
check
check
check
B
A
Z
I
O
D
CLK
Q
D
CLK
Q
D
CLK
Q
PLL
Div
IN1
CLK1
IN2
CLK2
OUT
A
B
Z
GATE
A
B
Z
I
O
I
O
Setup/Hold Check

## Slide 24: 设计过程——版图后处理
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test

## Slide 25: 设计过程——制造
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
Mask
Lens
Lens
Light source
Wafer
Projection
Illumination
Immersion
https://en.wikipedia.org/wiki/Back_end_of_line
: Resolution;
: Resolution Constant ();
: Wavelength;
: Numerical Aperture.

## Slide 26: 设计过程——封装测试
System Specifications
Functional Design
Logic Synthesis
Tech Mapping
Physical Design
Physical Verification
Sign Off
Layout Processing
Fabrication
Architectural Design
Package and Test
http://ece-research.unm.edu/jimp/vlsi_test/slides/html/overview1.htm

## Slide 27: IC设计流程

## Slide 28: 摩尔定律
每隔2年，芯片中晶体管数量将翻倍，晶体管大小缩小一半
高通48核Centriq，拥有超过180亿个晶体管
CPU系列 | 酷睿i9 11代系列
CPU主频 | 3.5GHz
最高睿频 | 5.3GHz
三级缓存 | 16MB
核心数量 | 八核心
线程数 | 十六线程
热设计功耗 | 125W
晶体管数量 | 70亿
工艺 | 14nm
面积 | 37.5×37.5mm
内存 | DDR4 3200MHz
指令 | 64位指令
内存带宽 | 50GB/s
Intel 4004
1971年1月 霍夫
4位微处理器
2250个晶体管
3mm×4mm
性能远超ENIAC
200美元
740 kHz
加两个8位数需850μs
12位地址
8位指令
640字节RAM
包含16个寄存器
第一颗
当前最强

## Slide 29: 工艺演化
https://semiengineering.com/imecs-plan-for-continued-scaling/
材料器件：用于缩小沟道宽度，减少MOS管大小，进而减小单元大小，以从设计上实现尺寸摩尔定律
  Dense Metal Pitch, Cu BEOL, Strained Si, Metal Gate, FinFets, GAA Nanosheets, CFet, Complex Stacked
光刻机：用于制造芯片，能够保证波长不断缩小，进而提高Pattern分辨率，以从制造上实现尺寸摩尔定律
  UV 365nm i-line, 248nm KrF，193nm DUV ArF, DUV Immersion, DUV-MP, 13.5nm EUV, EUV-MP, High-NA EUV
800-250
180-130
130-65
65-28
28-7
7-2

## Slide 30
未来趋势
规模会继续缩小：
  Buried power rail (BPR) power instead of distribution in interconnect;
  Transistors move to gate all around nanosheets (for higher drive, lower leakage);
  Using forksheets or CFET (complementary FET) to move the P and N transistors closer (4 Track);
关键材料至关重要：
  Two-dimensional channel materials such as MoS2（二硫化钼）
  For interconnect, we need a hybrid solution with a second metal like ruthenium （钌） (and a thinner barrier);
3D结构设计：
  EDA tools for 3D SOC design；
  Partition of Cache and Logic；
  Back-Side Power Distribution.

## Slide 31: 工艺参数
Technology | 65 nm | 45 nm | 32 nm | 22 nm | 14 nm | 10 nm
Year of Use | 2005 | 2007 | 2009 | 2011 | 2013 | 2015
Device’s | IBM FPGA | Xeon | 4i | Intel Core7 | iPhone 6s | TSMC
Frequency | 1.8 GHz. | 1.8 GHz | 1.8 GHz | 1.8-3.0 GHz | 3.8 GHz | 3.8-4.0GHz
Gate Length | 35 nm | 30 nm | 25 nm | 18 nm | 12 nm | 9 nm
Kgate /mm2 | 0.8 | 1.5 | 2.8 | 5.2 | 9.0 | 16.0
Technology Node | 90 nm | 65 nm | 45 nm | 22 nm
Fab Cost in billions of dollars | 2.8 | 3.8 | 6.9 | 9.5
Process Development cost in billions | 2.2 | 2.6 | 3.2 | 6.8
Node | 28 nm | 20 nm | 10 nm | 7 nm immersion | 7 nm EUV
Lithography Steps | 6 | 8 | 23 | 34 | 9
Overlay Metrology | 7 | 9-11 | 36-40 | 59-65 | 12
Key CMOS Technology Parameters
Mask Steps currently used in various Technology Nodes
Cost of Technology

## Slide 32: 市场需求
https://omdia.tech.informa.com/OM014575

## Slide 33: TSMC供应

## Slide 34: 110nm工艺新特性
单元库
  1. 重视时序库，功耗库，噪声库
物理设计
  2. 版图规划考虑划分
  3. 提出时序驱动， SI驱动的布局
  4. 考虑有用偏差的时钟树综合
  5. 考虑天线效应规则，预防SI布线
  6. 布线后优化WLM, DRV
签核分析
  7. RC参数提取考虑三维模型
  8. 考虑SI的精确静态时序分析模型
  9. 考虑最好和最坏的Corner进行检查
  10. 静态功耗和动态功耗分析
验证
  11. 物理验证包含DRC, ERC, LVS
  12. 基于扫描的逻辑等价检查
Logic Synthesis
Logic Compiling
Logic Optimization
Tech Mapping
12. Equivalence Checking
Analysis
8. 9. Timing Analysis
7. RC Extraction
10. Power
Noise
Layout Post Processing
RET/OPC/ILT
Post Simulation
Mask Generation
Physical Design
2. Floorplan
3. Placement
4. Clock Tree Synthesis
5. Routing
6. ECO
Physical Verification
11. ERC
11. DRC
11. LVS
Std Cell Lib
Device Modeling
1. Parasitic Extraction
DRC/LVS
System Specifications
Architectural Design
Functional Design
Simulation
Simulation (Circuit)
Emulation (System)
Fabrication
Package and Test
Chip

## Slide 35: 55nm工艺新特性
单元库
  1. 考虑不同电源电压阈标准单元库
  2. 电源切断技术；
物理设计
  3. 版图规划IO区域设计，多芯片封装；
  4. 考虑Clock Gate控制时钟树综合；
  5. 状态保持电源门控制技术；
  6. 功耗驱动布线；
  7. 考虑MMMC和良率的设计优化技术；
签核分析
  8. 考虑DFM，OPC的RC参数提取；
  9. 考虑MMMC和AOCV的时序检查；
  10. 多电源多电压和切断电源功耗分析；
验证
  11. 物理验证考虑DFM, OPC和良率
  12. 考虑DFT和ECO的形式验证
Logic Synthesis
Logic Compiling
Logic Optimization
Tech Mapping
12. Equivalence Checking
Analysis
9. Timing Analysis
8. RC Extraction
10. Power
Noise
Layout Post Processing
RET/OPC/ILT
Post Simulation
Mask Generation
Physical Design
3. Floorplan
Placement
4. 5. Clock Tree Synthesis
6. Routing
7. ECO
Physical Verification
11. ERC
11. DRC
11. LVS
Std Cell Lib
2. Device Modeling
1. Parasitic Extraction
DRC/LVS
System Specifications
Architectural Design
Functional Design
Simulation
Simulation (Circuit)
Emulation (System)
Fabrication
Package and Test
Chip

## Slide 36: 28nm工艺新特性
单元库
  1. 会考虑SOI技术或FinFet器件模型，即Pcell变得复杂；
  2. 考虑器件米勒效应；
物理设计
  3. 考虑图依赖效应布局；
  4. 考虑DP和通孔可靠性的布线；
  5. 考虑DRC，EM和串扰的布线；
  6. 布线后优化考虑DVI, DFI, LDE；
  7. 考虑修时序设计优化技术；
签核分析
  8. 考虑耦合电容的参数提取；
  9. 考虑MMMC和SSTA的时序检查；
  10. 分析电压降
验证
  11. 物理验证考虑多重光刻的设计规则；
  12. 进行ESD和电流密度检查；
Logic Synthesis
Logic Compiling
Logic Optimization
Tech Mapping
Equivalence Checking
Layout Post Processing
RET/OPC/ILT
Post Simulation
Mask Generation
Physical Design
Floorplan
3. Placement
Clock Tree Synthesis
4. 5. Routing
6. ECO
Physical Verification
ERC
11. DRC (MP)
LVS
Std Cell Lib
1. Device Modeling
2. Parasitic Extraction
DRC/LVS
System Specifications
Architectural Design
Functional Design
7. Timing Optimization
12. ESD/CD
Analysis
9. Timing Analysis
8. RC Extraction
Power
Noise
10. IR Drop
Simulation
Simulation (Circuit)
Emulation (System)
Fabrication
Package and Test
Chip

## Slide 37
背景目标
设计思路
设计内容
设计方式
01
02
03
04

## Slide 38: 开源EDA工具目标和任务
    研用结合：实用牵引，以用带研，研以致用
    A. EDA基础设施：软件基础组件，如：文件、解析器、数据库、基础数据结构等，供EDA工具使用
    B. EDA点工具：完成各个功能的工具模块，如：逻辑综合、布局布线、物理验证等
    C. 芯片设计流程：一套用于设计芯片版图的智能自动化流程，通过调用EDA工具的接口命令完成芯片设计
    D. 测试芯片集：构建覆盖多种规模、多种场景，具备多种粒度的基准测试集
    E. 工艺库：工业级可生产的开源工艺库和单元库，是推动开源EDA发展的重要保障
    F. 研发生态：开源EDA平台聚集国内优势力量，推动科学研究提供了新的思路（水滴石穿计划）
    G. 应用生态：推动形成典型应用场景，由教学场景入手（一生一芯计划），逐步打造产品级示范应用
  从低工艺(110nm)，至更高工艺(55nm/28nm, 甚至14nm)
从小规模SoC芯片(数十万门)，到更大规模(上千万到上亿)
从部分单点EDA设计工具，到完整EDA设计+验证工具链
从EDA工具可用，工具功能完善可靠，到工具质量和性能良好
iEDA
C.芯片设计流程
A.EDA基础设施
D.测试芯片集
E.
工艺库
G.应用生态
F.研发生态
B.EDA工具
电路仿真
逻辑综合
物理设计
签核分析
物理验证
版图处理
单元设计

## Slide 39: 开源EDA项目的几条线
问题拆解
框架和平台
关键技术
学术界经典问题
EDA和芯片设计企业
问题拆解中的关键问题
自研
开放课题
比赛
技术成果
实现代码原型
摸清工具原理
跑通
架构设计质量高
可完成 RTL-GDSII 的开源EDA平台
代码和文档质量高
对口企业
国内骨干EDA企业和芯片设计企业
助力科研
支持新型工艺
（硅光）
构建生态

## Slide 40: EDA工具：问题拆解
EDA Platform
EDA Modules
Tools
Sub-Tools
Steps
Operators
EDA Flow
Logic Synthesis
Physical Design
Sign Off
Physical Verification
Layout Processing
Logic Compiling
Logic Optimization
Tech Mapping
Floorplan
Placement
CTS
Routing
STA
Power Analysis
Noise Analysis
DRC / ERC
LVS
OPC / RET
Mask Generation
……
Initial Placement
Global Placement
Post Global Placement
Legalization
Detail Placement
Assign Cell to Right Region
Cell Respread
Align Cell to Row
Reorder Cell in a Row
Spread Cell in a Row
Greedy
Refinement
Check Legality
……
……
……
……
……
……
……
……
Tetris
Dynamic Programming
Quadrable Programming
Linear Programming
Local Search Method
开源EDA平台拆解分为六级进行：EDA工具平台，EDA工具模块，EDA工具，EDA子工具，工具内步骤，独立问题和算子（白皮书）
1个EDA平台
7个主要方向
9大功能模块
45个工具
101个子工具
>600个步骤
>2000个问题
>1万个解决方案

## Slide 41: Modules and Tools
Modules | Tools/ |  |  |  |  | 
Simulation | Circuit Simulation | RTL Simulation | FPGA Simulation | System Emulation | Device TCAD | Debug
Logic Synthesis | Logic Compilation | Logic Represent | Logic Optimization | Tech Map | Test Insertion | Equivalence Verification
Physical Design | Floorplan | Placement | CTS | Timing Optimization | Routing | ECO
Verification | DRC | ERC | ESD | Antenna Effect | Current Density | LVS
Sign Off | RC Extraction | STA | Power | IR Drop | Noise | Electro Migration
Layout Process | DFM | Via/Metal Reliable | Test Pattern | Hotspot | RET/OPC/ILT | Mask Generation
Package & Test | Wafer Test | Die Test | Beyond Die | 2.5D/3D Package | Package Test | System Test
Database | Files | Parsers | Data Structure | Database | Manager | Service
Flow | Interface | GUI | Script | Flow | Architect | Intelligent Platform
Benchmark | Library (PDK/SCL) | RTL Designs | Modules Benchmark | Tools Benchmark | Steps Benchmark | Problems Benchmark
Operator | Numerical Calculation | PDE | Optimization | Combinatorial Optimization | Algebra Combination | NP-Hard

## Slide 42: EDA工具：关键技术
六步骤拆解EDA工具，抽象为去EDA属性的小颗粒的数学，算法，软件和性能问题。形成关键技术问题，并描述成白皮书。

## Slide 43: EDA工具：框架
物理设计
全局布局
布局

## Slide 44: iPD-EDA软件架构
数据配置层
数据构建层
数据库
用户交互
业务功能
GUI
Network
Library
Timing
Tech
Design
Layout
.v(RTL) / .v(netlist) / .def / .lef / .lib / .sdc / .spef / .sdf / .gds / .sp / .model …
文件解析器
共有数据访问接口层
（支持所有业务数据）
数据源
配置参数
工具模块数据访问层
LS, MAP, FP, GP, DP, TO, CTS, GR, DR, DRC, ERC, LVS, RCX, STA, NA, PA
数据库
管理
兼容
模块
Shell/TCL/Python
Flow
公共数据
私有数据
业务交互层
数据结构
数值优化
算法库
加速器
性能
线程池
高性能计算库
并行计算
异构计算
…
功能模块
数值计算
图计算
组合优化
逻辑运算
运筹规划
微分方程
智能学习
启发式
异常处理
Log
Report
辅助模块
Test
Utility
LS
MAP
PS
DP
FP
CTS
TO
GR
核心工具模块
模块交互业务管理
策略管理
GP
DR
DRC
RCX
LVS
STA
PA
测试集